Contents

Overview	4

Features	4

Plug-in Connections	5

How Turn-O-Matic systems work	6

V3 system configurations and features	7

S3 base systems	7

S3 expansions, hard-wired Push Button	8

S3 expansions, wireless Push Button	9

M3 base system	10

M3 expansions	11

M3 Par (parallel service points)	12

M3 Par expansions	13

M3 Par expansion option – SP Indicators	14

M3 Par expansion option – SL900 service position lamps	15

L3 base system	16

L3 expansions	17

L3 multiple services	18

L3 Par (parallel service points)	19

L3 Par expansion option – SP Indicators	20

L3 Par expansion option – SL900 service position lamps	21

L3 expansion options – info Indicators	22

L3 Par expansion option – service position help call Indicator	23

V3 installation, connections and address setting	24

Power connections	24

I/O connections	25

Setting TOM-Net addresses	26

V3 installation, TOM-Net address settings	27

S3 base systems, address settings	27

S3 expansions, hard-wired Push Button, address settings	28

S3 expansions, wireless Push Button, address settings	29

M3 base system, address settings	30

M3 expansions, address settings	31

M3 Par (parallel service points), address settings	32

M3 Par expansions, address setttings	33

M3 Par expansion option – SP Indicators, address settings	34

M3 Par expansion option – SL900 service position lamps, address settings	35

L3 base system, address settings	36

L3 expansions, address settings	37

L3 multiple services, address settings	38

L3 Par (parallel service points), address settings	39

L3 Par expansion option – SP Indicator, address settings	40

L3 Par expansion option – SL900 service position lamps, address settings	41

L3 expansion options – info Indicators, address settings	42

L3 Par expansion option – service position help call Indicator, address setting	43

Approximate installation times for V3 START and PLUS packs	44

V3 system messages	45

Indicator error messages	45

K900 error messages	46

K900 warning messages, L3 system	47

V3 products in V2 system configurations	49

Direct 900 – replacement Indicator	49

Direct 900 – expansion Indicator	50

Direct 900 Parallel – replacement Indicator	51

Direct 900 Parallel – expansion Indicator	52

Select 900  – replacement Indicator	53

Select 900  – expansion Indicator	54

Select 900  – K900 replacement for C900	55

Select 900 Parallel  – replacement Indicator	56

Select 900 Parallel – K900 replacement for C900	57

Select 900 Parallel  – expansion SP Indicator and K900	58

Signal and Info 900  – D900A3 replacement for D900A or D90E	59

Signal and Info 900  – replacement Indicator	60

Signal and Info 900  – K900 replacement for C900	61

Signal and Info 900 Parallel  – expansion SP Indicator and K900	62

Signal and Info 900  – expansion with K900	63

Connection adapter V2 cable - V3 RJ10 plug, pin out	64

# Overview

## Features

Turn-O-Matic V3 products and systems were developed to improve and expand the current V2 range with new features, cost savings and quality improvements while retaining the best current features.  Major new features across the V3 product line are:

- Simple, plug-in installation for lower installed costs

- Improved, more tolerable electronics for lower warranty and service costs

- Small S3 system; low cost plug&play sequential service system with top of the line features

- Medium M3 system; deluxe features at low cost for sequential or selected service at up to 15 parallel service points

- Large L3 system; competitive multiple service alternative (up to 5 service types) with real-time and statistical data information for service at up to 30 parallel service points.

Still retaining the most valuable V2 features:

- Safe, low-voltage units

- Modular products for flexible system configuration

- Simple, reliable 2-wire data transmission allowing networks over 500 meters long

## Plug-in Connections

All V3 units have plug-in connection ports, type DC jack and RJ10 jack.

## How Turn-O-Matic systems work

Every system with more than one electronic unit (Indicator, K900, SL900, D900A3 or SC900) is a data network, type RS485 using a Master-Slave communications protocol.   Each TOM unit includes an RS485 transceiver for receiving and transmitting digital data, with 2 data ports for plug-in linking on the Turn-O-Matic network (TOM-Net) as a serial chain, typically called a ‘daisy chain’ as illustrated below.

In addition to the data connections shown, each TOM-Net unit requires power; 12VAC or 15VDC.

The importance of using proper data cabling:

The RS485 data circuit can be affected by the increasing amount of interference present in today’s environment; electromagnetic (EMI), electrostatic (ESI) and radio frequency (RFI) interference.  To minimise the interference effects, Turn-O-Matic data cable is shielded, twisted pair, type LiY-CY, min. size 2 x 0.14 mm (26 AWG).  To provide a continuous reference ground for the RS485 data signal, the cable shield is also used as a signal ground and is connected at each unit.

Using a lower quality cable for TOM-Net data cable or making lower quality connections may work without problems in some installations, but never in all installations.

# V3 system configurations and features

## S3 base systems

- Set starting service number; take a ticket from dispenser and set Indicator display to ticket number.  Hold down Push Button (+) to increase displayed number +10, press once to increase number +1, press Push Button (-) to decrease number –1.

- Service turn reservation; arriving customers take sequentially numbered ticket from dispenser.

- Call customers for service; press Push Button (+) to increase displayed service number on Indicator +1.

- Indicator saves last displayed number in non-volatile memory on power OFF and displays saved number on new power ON.

- Indicator display flashes on number change +1; number of flashes is set-up selectable from 0 = no flashing to 9 = continuous flashing.

- Indicator sounds a tone on number change +1; tone type and volume is selectable via dip switches on back of Indicator.

- Indicator display update can be delayed on multiple Push Button presses; display update is set-up selectable from 0 to 29 seconds.

- Indicator display can shut OFF (SLEEP) on no activity; time to SLEEP is set-up selectable from 0 = No SLEEP to 99 minutes.

## S3 expansions, hard-wired Push Button

- Indicator PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- Extended display of called service number; PLUS pack SLAVE Indicators display same number as the START pack MASTER Indicator.

- Multiple Push Button input, press any Push Button (+) to increase displayed service number on Indicator(s) +1.   Use power ON set-up on MASTER Indicator to set Indicator(s) display update delay on multiple Push Button presses.  MASTER Indicator can buffer up to seven (7) Push Button presses.

## S3 expansions, wireless Push Button

- Indicator PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- Extended display of called service number; PLUS pack SLAVE Indicators display same number as the START pack MASTER Indicator.

- Multiple Push Button input, press any Push Button (+) to increase displayed service number on Indicator(s) +1.   Use power ON set-up on MASTER Indicator to set Indicator(s) display update delay on multiple Push Button presses.  MASTER Indicator can buffer up to seven (7) Push Button presses.

- Wireless Push Buttons are digitally coded to eliminate cross talk between neighbouring systems.  Expansion Wireless Push Button codes must be recorded in the Receiver on the MASTER Indicator to be recognised by the system.

## M3 base system

- Set starting service number; take a ticket from dispenser and set start number on the K900.  Hold down F key 2+ seconds, key in ‘2 0’, press ENTER, key in ticket number, press F to save and exit.

- Service turn reservation; arriving customers take sequentially numbered ticket from dispenser.  Alternatively, for order pick-up service, last two digits of customer receipt can be used for selectively calling service turn number when order is ready.

- Call customers sequentially for service; press K900 ENTER key to increase displayed service number on K900 and Indicator +1.  To decrease service number, press R key on K900 (no Indicator display).

- Call customers selectively for service; key in number on K900 and press ENTER key to display number on K900 and Indicator.

- Save customers for ‘Repeat Display’; with service number displayed on K900, press S key or use set-up option for ‘Automatic’ saving on calling for service.  Up to 20 numbers can be repeated on the Indicator from 0 = no ‘Repeat Display’ to 9 = continuously repeating.

- Remove customer from ‘Repeat Display’; key in service number on K900 and press E key.

- K900 saves last called number in non-volatile memory on power OFF and displays saved number on new power ON.

- Indicator display flashes on number change; number of flashes is set-up selectable from 0 = none to 9 = continuous flashing.

- Indicator sounds a tone on number change; tone type and volume is selectable via dip switches on back of Indicator.

- Indicator display update for multiple K900 entries and ‘Repeat Display’; update delay is selectable from 0 to 29 seconds.

- Indicator display can shut OFF (SLEEP) on no activity; time to SLEEP is set-up selectable from 0 = No SLEEP to 99 minutes.

## M3 expansions

- Indicator and K900 PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- Extended display of called service number; PLUS pack Indicators display same number as the START pack Indicator.

- Multiple K900 inputs; press any K900 ENTER key to increase displayed service number on Indicator(s) +1 or call any selected number from any K900.  Indicator(s) display update delay on multiple K900 calls is set-up selectable from 0 to 99 seconds.  MASTER K900 can buffer up to twenty (20) multiple number inputs.

## M3 Par (parallel service points)

- Set starting service number; take a ticket from dispenser and set start number on the MASTER K900.

- Service turn reservation; arriving customers take sequentially numbered ticket from dispenser.  Alternatively, for order pick-up service, last two digits of customer receipt can be used for selectively calling service turn number when order is ready.

- Call customers sequentially for service; press K900 ENTER key to increase service number +1 and display called service number and calling service point number (SP) on CD display.  To decrease service number, press R key (no Indicator display).

- Call customers selectively; key in number on K900 & press ENTER to display service number and SP number on CD display.

- Save customers for ‘Repeat Display’; with service number displayed on K900, press S key or use set-up option for ‘Automatic’ saving on calling for service.  Up to 20 numbers can be repeated on the Indicator from 0 = no ‘Repeat Display’ to 9 = continuously repeating.

- Remove customer from ‘Repeat Display’; key in service number on K900 and press E key.

- K900 saves last called number in non-volatile memory on power OFF and displays saved number on new power ON.

- CD display flashes on number change; number of flashes is set-up selectable from 0 = none to 9 = continuous flashing.

- CD display ‘number’ Indicator sounds a tone on number change; tone type and volume is selectable via dip switches on back of Indicator.

- CD display update for multiple K900 entries and ‘Repeat Display’; update delay is selectable from 0 to 29 seconds.

- CD display can shut OFF (SLEEP) on no activity; time to SLEEP is set-up selectable from 0 = No SLEEP to 99 minutes.

## M3 Par expansions

- Indicator and K900 PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- Extended display of service number and calling SP number; PLUS pack CD Indicators display same numbers (called service number and calling SP number) as the START pack CD Indicators.

- Multiple K900 inputs; press any K900 ENTER key to increase displayed service number on Indicator(s) +1 or call any selected number from any K900.   Use function setting F33 to set Indicator(s) display update delay on multiple K900 calls.  MASTER K900 can buffer up to twenty (20) multiple number inputs.

## M3 Par expansion option – SP Indicators

- Indicator PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- Service Point (SP) Indicators display last called service number at the SP.  Number remains displayed until the next service call at that SP.

- Inactive service points can automatically shut off their SP Indicator (SLEEP); time to SLEEP is set-up selectable from 0 = No SLEEP to 99 minutes.

## M3 Par expansion option – SL900 service position lamps

- SL900 PLUS pack includes plug-in Power supply and plug-in TOM-Net data cables.

- Service Point (SP) signal lamps guide customers to calling service point.  SL900 at calling service point blinks on service call at that SP and then remains steady lit for an additional time.  SL900 blink and steady-lit time durations are set-up selectable; blinking time from 0 to 99 seconds and steady-lit time from 0 to 99 seconds.

## L3 base system

- Indicator, D900A3 and K900 PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- Set starting service number; take a ticket from dispenser with cover open and set start number on the K900 after it is logged on.

- Service turn reservation; arriving customers take sequentially numbered ticket from dispenser, which automatically registers the ticket in the SC900 and presents the next ticket.

- Customers waiting info; pressing the ?W key on the K900 displays number of customers waiting.

- Call customers sequentially for service; press K900 ENTER key to increase displayed service number on K900 and Indicator +1.  If there are no waiting customers, K900 displays  - 0 - and does not increase the service number.

- Priority call customers for service; key in number on K900 and press ENTER key to display number on K900 and Indicator.

- Save customers for recall; press S key on the K900 or use set-up option for ‘Automatic’ saving.

- Recall saved customers; press R key on K900 to scroll recall numbers and press ENTER to recall or key in recall number and press R key.

- Service transaction data; SC900 saves date and time when ticket number was dispensed, called for service and when service was completed.  This data can be uploaded using the included Turn-O-View 3 software to view and print service statistics.

- Mark customer type; press ?1 ... ?5 key on K900 to mark customer or inquiry type, including marking NO SHOW customers.

- Indicator display flashes on number change; number of flashes is set-up selectable from 0 = none to 9 = continuous flashing.

- Indicator sounds a tone on number change; tone type and volume is selectable via dip switches on back of Indicator.

- Indicator display update for multiple K900 service calls; update delay is selectable from 0 to 99 seconds.

- Indicator display can shut OFF (SLEEP) on no activity; time to SLEEP is set-up selectable from 0 = No SLEEP to 99 minutes.

## L3 expansions

- Indicator, K900 and SL900 PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- Extended display of called service number; PLUS pack Service Indicators display same number as the base PLUS pack Indicator.

- Separate recall service Indicator; a separate Indicator can be used for directing recall service customers to another location or to distinguish recall service from normal service calls.

- Multiple K900 input; press any K900 ENTER key to increase displayed service number on Service Indicator(s) +1 or call any selected number from any K900.  Indicator display update delay on multiple K900 calls is set-up selectable from 0 to 99 seconds.  MASTER K900 can buffer up to twenty (20) multiple number inputs.

- Customers waiting signal; Help Customers Waiting (HCW) SL900 lamps light up when there are customers waiting for service.  SL900 lamps blink when number of waiting customers reaches ‘Alert Signal’ level; selectable from 1 to 99 customers waiting.

- Customer waiting time option; HCW Alert Signal blinking level can be set to customer waiting time, selectable from 1 to 99 minutes waiting or alternatively from 10 to 990 seconds waiting.

## L3 multiple services

- Indicator, D900A3, K900 and SL900 PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- Multiple services in parallel; up to 5 ticket dispensers per system, each dispenser for a separate service type.

- Multiple services in series; service ticket numbers can be moved (saved) to the next available service type slot (without dispenser) for continuing service.  The receiving service type can then move service numbers to a third service type etc., using up to 4 service slots without dispenser for continuing service.  Service numbers moved to the next available service can either be saved for normal sequential call in the new service or saved for recall service in the new service type.

- Service Indicators are set to a specific service type and only display service numbers for that service type.

- Customers waiting signal is set to a service type; Help Customers Waiting (HCW) SL900 lamps light up when there are customers waiting for the specified service.  Each SL900 Alert Signal can be set (addressed) to a different specified service type.

- Info Indicators are set to a service type: Info Indicator display AWT, DSN or HCW information for the specified (addressed) service.

- Service type switching for service staff; each K900 can be logged into any of the 5 service types, allowing service staff to switch over to help other service types if there are many waiting customers.

## L3 Par (parallel service points)

- Indicator, D900A3 and K900 PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- Set starting service number; take a ticket from dispenser with cover open and set start number on any logged-on K900.

- Service turn reservation; customers take a ticket from dispenser, number is registered and next ticket is presented automatically.

- Customers waiting info; pressing the ?W key on the K900 displays number of customers waiting.

- Call customers sequentially for service; press K900 ENTER key to increase service number +1 and display service number plus calling SP number on the CD display.  If there are no waiting customers, K900 displays  - 0 -.

- Priority calling; key in number and press ENTER key on K900 to display service number and calling SP number on CD display.

- Save customers for recall; press S key on the K900 or use set-up option for ‘Automatic’ saving.

- Recall customers; press R key on K900 to scroll recall numbers and press ENTER to recall or key in recall number and press R.

- Service transaction data; SC900 saves date and time when ticket number was dispensed, called for service and when service was completed.  This data can be uploaded using the included Turn-O-View 3 software to view and print service statistics.

- Mark customer type; press ?1 ... ?5 key on K900 to mark customer or inquiry type, including marking NO SHOW customers.

- Set alias number for SP; each K900 can be set to a 3-digit alias SP number (room number, for example), no duplicates allowed.

- CD display flashes display and sounds a tone on number change; number of flashes, tone type and tone volume are selectable.

- CD display sounds a tone on number change; tone type and volume is selectable via dip switches on back of Indicator.

- CD display update for multiple K900 service calls; update delay is selectable from 0 to 99 seconds.

- CD display can shut OFF (SLEEP) on no activity; time to SLEEP is set-up selectable from 0 = No SLEEP to 99 minutes.

## L3 Par expansion option – SP Indicators

- Indicator PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- Service Point (SP) Indicators display last called service number at the SP.  Number remains displayed until the next service call at that SP.

- Inactive service points can automatically shut off their SP Indicator (SLEEP); time to SLEEP is set-up selectable from 0 = No SLEEP to 99 minutes.

## L3 Par expansion option – SL900 service position lamps

- SL900 PLUS pack includes plug-in Power supply and plug-in TOM-Net data cables.

- Service Point (SP) signal lamps guide customers to calling service point.  SL900 at calling service point blinks on service call at that SP and then remains steady lit for an additional time.  SL900 blink and steady-lit time durations are set-up selectable; blinking time from 0 to 99 seconds and steady-lit time from 0 to 99 seconds.

## L3 expansion options – info Indicators

- Indicator PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- Advised waiting time info; Advised Waiting Time (AWT) Indicator displays the currently calculated wait for service using the rolling average of the last 10 customers served.  The calculated Advised Waiting Time can be manually changed at any time from a K900.

- Last dispensed ticket number info; Dispensed Service Number (DSN) Indicator displays the last dispensed ticket number.

- Customers waiting info; Help Customers Waiting (HCW) Indicator displays the number of customers waiting for service.

- Customer waiting time option; HCW Indicator can be set to display customer waiting time in minutes or in seconds.

## L3 Par expansion option – service position help call Indicator

- Indicator PLUS pack includes plug-in Power supply and plug-in TOM-Net data cables.

- Call for help to Service Point (SP); pressing the ! (Attention) key on a K900 displays the K900’s SP number (or SP alias number if set) on the Help Service Position (HSP) Indicator.  K900 displays ‘H.nnn’  (nnn = last called number) to show that it is in HSP mode, during which normal operation is suspended.  Pressing the ! key again exits HSP mode and stops display of the SP number on the HSP Indicator.

- Urgent call for Help to SP: holding down the ! key on a K900 for 3+ seconds displays the K900’s SP number or alias number continuously blinking on the HSP Indicator.  K900 display blinks ‘H.nnn’ to show that it is in urgent HSP mode.  Pressing the ! key again exits HSP mode and stops display of the SP number on the HSP Indicator.

# V3 installation, connections and address setting

## Power connections

## I/O connections

## Setting TOM-Net addresses

# V3 installation, TOM-Net address settings

## S3 base systems, address settings

## S3 expansions, hard-wired Push Button, address settings

## S3 expansions, wireless Push Button, address settings

## M3 base system, address settings

## M3 expansions, address settings

## M3 Par (parallel service points), address settings

## M3 Par expansions, address setttings

## M3 Par expansion option – SP Indicators, address settings

## M3 Par expansion option – SL900 service position lamps, address settings

## L3 base system, address settings

## L3 expansions, address settings

## L3 multiple services, address settings

## L3 Par (parallel service points), address settings

## L3 Par expansion option – SP Indicator, address settings

## L3 Par expansion option – SL900 service position lamps, address settings

## L3 expansion options – info Indicators, address settings

## L3 Par expansion option – service position help call Indicator, address setting

# Approximate installation times for V3 START and PLUS packs

NOTE: Approximate installation times are assuming that usable mains power outlets are available for direct plug-in of power supplies.   Time for training service personnel on system operation is not included; normally, approx. training time = 1 – 2 hours for S3 system, 2 – 3 hours for M3 system and 3 – 5 hours for L3 system.

| System | START packs | Approximate installation time in hours | PLUS packs | Approximate installation time in hours |
| --- | --- | --- | --- | --- |
| S3 | S32 PB, S33 PB (with or w/o CS) | 1 – 2 | IN902 X1, IN903 X1 | 1 – 2 |
|  | S32 RF, S33 RF (with or w/o CS) | ½ - 1 | IN902 X2, IN903 X2 | 2 – 3 |
|  | S323 PB | 2 – 3 | IN902 X2CB, IN903 X2CB | 3 – 4 |
|  | S323 PB CB | 3 – 4 | IN902 X3CB, IN903 X3CB | 3 – 4 |
|  | S323 RF | 1½ - 2 |  |  |
|  | S323 RF CB | 2½ - 3 |  |  |
| M3 | M32, M33 (with or w/o CS) | 1 – 2 | IN902 X1, IN903 X1 | 1 – 2 |
|  | M32 Par, M33 Par | 3 – 4 | IN902 X2, IN903 X2 | 2 – 3 |
|  |  |  | IN902 X2CB, IN903 X2CB | 3 – 4 |
|  |  |  | IN902 X3CB, IN903 X3CB | 3 – 4 |
|  |  |  | CD22, CD32 | 2 – 3 |
|  |  |  | K900 | 1 – 2 |
|  |  |  | SL900 x2 | 2 – 3 |
| L3 | L3 incl. system setup & TOV install | 4 – 5 | D900A3 | 1 – 2 |
|  |  |  | K900 | 1 – 2 |
|  |  |  | IN902 X1, IN903 X1 | 1 – 2 |
|  |  |  | IN902 X2CB, IN903 X2CB | 3 – 4 |
|  |  |  | IN902 X3CB, IN903 X3CB | 3 – 4 |
|  |  |  | CD22, CD32 | 2 – 3 |
|  |  |  | K900 | 1 – 2 |
|  |  |  | SL900 x2 | 2 – 3 |

# V3 system messages

## Indicator error messages

## K900 error messages

## K900 warning messages, L3 system

K900 warning messages, L3 system

# V3 products in V2 system configurations

## Direct 900 – replacement Indicator

- Indicator V2service pack includes plug-in V2 cable adapters for connecting existing V2 power supply and TOM-Net data cables to the V2service Indicator.

- For replacement of a V2 MASTER Indicator, set the V2service Indicator address = 21.

- For replacement of a V2 MASTER Indicator with Wireless Push Button RFv2, install the RFv2 Receiver on the V2service Indicator.

- For replacement of a V2 SLAVE Indicator, set the V2service Indicator address = 20.

- Connect existing power cable to the V2service Indicator with the ‘Connection adapter V2 cable - V3 DC plug’.

- Connect the existing push button cable to the V2service Indicator with the ‘Connection adapter V2 cable - V3 RJ10 plug’.   Connect one lead to Pin 2 – Signal and the other lead to Pin 3 - GND.

- Connect the existing data cable to the V2service Indicator with the ‘Connection adapter V2 cable - V3 RJ10 plug’.   Connect the WHITE lead to Pin2-Signal A, brown lead to Pin3-Signal B and the cable shield to Pin1-GND.

## Direct 900 – expansion Indicator

- Indicator PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- Extended display of called service number; PLUS pack SLAVE Indicators display same number as the START pack MASTER Indicator.

- Set PLUS pack expansion Indicator to address = 20.

- To connect the PLUS pack TOM-Net data cable to the V2 Indicator, cut off the RJ10 plug on the V2 Indicator end of the cable.  Then, connect the data cable leads to the COMMS connector on the V2 Indicator as follows; WHITE lead to A, BROWN lead to B and the cable shield to the shield ground (upside down T).

## Direct 900 Parallel – replacement Indicator

- Indicator V2service pack includes plug-in V2 cable adapters for connecting existing V2 power supply and TOM-Net data cables to the V2service Indicator.

- For replacement of a V2 CD-Nr Indicator, set V2service Indicator address = 20.

- For replacement of a V2 CD-SP Indicator, set V2service Indicator address = 30.

- For replacement of V2 Service Point (SP) Indicators, set V2service Indicator address as follows:

SP1 = 21	SP2 = 22	SP3 = 23	SP4 = 24	SP5 =25	SP6 = 26	SP7 = 27	SP8 = 28

SP9 = 29	 SP10 = 2A	SP11 = 2B	SP12 =2C	SP13 = 2D	SP14 = 2E	SP15 = 2F

NOTE: Duplicate addresses are not allowed.

- For replacement of a V2 SP Indicator with Wireless Push Button RFv2, install the RFv2 Receiver on the V2service Indicator.

- Connect existing power cable to the V2service Indicator with the ‘Connection adapter V2 cable - V3 DC plug’.

- Connect the existing data cable to the V2service Indicator with the ‘Connection adapter V2 cable - V3 RJ10 plug’.   Connect the WHITE lead to Pin2-Signal A, brown lead to Pin3-Signal B and the cable shield to Pin1-GND.

## Direct 900 Parallel – expansion Indicator

- Indicator PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- Connect either the PB900 plug-in set OR install the Wireless Push Button set RFv2 on the PLUS pack Indicator.

- For expansion of Service Point Indicators, set PLUS pack Indicator address as follows:

SP1 = 21	SP2 = 22	SP3 = 23	SP4 = 24	SP5 =25	SP6 = 26	SP7 = 27	SP8 = 28

SP9 = 29	 SP10 = 2A	SP11 = 2B	SP12 =2C	SP13 = 2D	SP14 = 2E	SP15 = 2F

NOTE: Duplicate addresses are not allowed.

- To connect the PLUS pack TOM-Net data cable to the V2 Indicator, cut off the RJ10 plug on the V2 Indicator end of the cable.  Then, connect the data cable leads to the COMMS connector on the V2 Indicator as follows; WHITE lead to A, BROWN lead to B and the cable shield to the shield ground (upside down T).

## Select 900  – replacement Indicator

- Indicator V2service pack includes plug-in V2 cable adapters for connecting existing V2 power supply and TOM-Net data cables to the V2service Indicator.

- For replacement of a V2 Indicator, set the V2service Indicator address = 20.

- Connect existing power cable to the V2service Indicator with the ‘Connection adapter V2 cable - V3 DC plug’.

- Connect the existing data cable to the V2service Indicator with the ‘Connection adapter V2 cable - V3 RJ10 plug’.   Connect the WHITE lead to Pin2-Signal A, brown lead to Pin3-Signal B and the cable shield to Pin1-GND.

## Select 900  – expansion Indicator

- Indicator PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- Extended display of called service number; PLUS pack Indicator display same number as the V2 base Indicator.

- Set PLUS pack expansion Indicator to address = 20.

- To connect the PLUS pack TOM-Net data cable to the V2 Indicator, cut off the RJ10 plug on the connection to the V2 Indicator end of the cable.  Then, connect the data cable leads to the COMMS connector on the V2 Indicator as follows; WHITE lead to A, BROWN lead to B and the cable shield to the shield ground (upside down T).

## Select 900  – K900 replacement for C900

- Connect existing power cable to the K900 with the ‘Connection adapter V2 cable - V3 DC plug’.

- Set K900 address = 41.  During K900 start-up, hold down the L key to open the address setting routing.  Then, press the R key first to display the address selection 41.  Hold down the L key to save the new address setting, which takes effect on next power ON.

- Connect the existing data cable to the K900 with the ‘Connection adapter V2 cable - V3 RJ10 plug’.   Connect the WHITE lead to Pin2-Signal A, brown lead to Pin3-Signal B and the cable shield to Pin1-GND.

## Select 900 Parallel  – replacement Indicator

- Indicator V2service pack includes plug-in V2 cable adapters for connecting existing V2 power supply and TOM-Net data cables to the V2service Indicator.

- For replacement of a V2 CD-Nr Indicator, set the V2service Indicator address = 20.

- For replacement of a V2 CD-SP Indicator, set the V2service Indicator address = 30.

- For replacement of V2 Service Point (SP) Indicators, set the V2service Indicator address as follows:

SP1 = 21	SP2 = 22	SP3 = 23	SP4 = 24	SP5 =25	SP6 = 26	SP7 = 27	SP8 = 28

SP9 = 29	 SP10 = 2A	SP11 = 2B	SP12 =2C	SP13 = 2D	SP14 = 2E	SP15 = 2F

NOTE: Duplicate addresses are not allowed.

- Connect existing power cable to the V2service Indicator with the ‘Connection adapter V2 cable - V3 DC plug’.

- Connect the existing data cable to the V2service Indicator with the ‘Connection adapter V2 cable - V3 RJ10 plug’.   Connect the WHITE lead to Pin2-Signal A, brown lead to Pin3-Signal B and the cable shield to Pin1-GND.

## Select 900 Parallel – K900 replacement for C900

- Connect existing power cable to the K900 with the ‘Connection adapter V2 cable - V3 DC plug’.

- Set the K900 address.  During K900 start-up, hold down the L key to open the address setting routing.  Then, press the R key first to display the address selection starting with 41.   Select the applicable Service Point address as follows:

SP1 = 41	SP2 = 42	SP3 = 43	SP4 = 44	SP5 =45	SP6 = 46	SP7 = 47	SP8 = 48

SP9 = 49	 SP10 = 4A	SP11 = 4B	SP12 =4C	SP13 = 4D	SP14 = 4E	SP15 = 4F

NOTE: Duplicate addresses are not allowed.

Hold down the L key to save the new address setting, which takes effect on next power ON.

- Connect the existing data cable to the K900 with the ‘Connection adapter V2 cable - V3 RJ10 plug’.   Connect the WHITE lead to Pin2-Signal A, brown lead to Pin3-Signal B and the cable shield to Pin1-GND.

- NOTE: Service Point direction lamps cannot be used with K900 units in V2 systems.

## Select 900 Parallel  – expansion SP Indicator and K900

- Indicator PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- For expansion of Service Point Indicators, set PLUS pack Indicator address as follows:

SP1 = 21	SP2 = 22	SP3 = 23	SP4 = 24	SP5 =25	SP6 = 26	SP7 = 27	SP8 = 28

SP9 = 29	 SP10 = 2A	SP11 = 2B	SP12 =2C	SP13 = 2D	SP14 = 2E	SP15 = 2F

NOTE: Duplicate addresses are not allowed.

- For expansion of Service Point keypads, set PLUS pack K900 address as follows:

SP1 = 41	SP2 = 42	SP3 = 43	SP4 = 44	SP5 =45	SP6 = 46	SP7 = 47	SP8 = 48

SP9 = 49	 SP10 = 4A	SP11 = 4B	SP12 =4C	SP13 = 4D	SP14 = 4E	SP15 = 4F

NOTE: Duplicate addresses are not allowed.

- To connect the PLUS pack TOM-Net data cable to the V2 Indicator, cut off the RJ10 plug on the V2 Indicator end of the cable.  Then, connect the data cable leads to the COMMS connector on the V2 Indicator as follows; WHITE lead to A, BROWN lead to B and the cable shield to the shield ground (upside down T).

- NOTE: Service Point direction lamps cannot be used with K900 units in V2 systems.

## Signal and Info 900  – D900A3 replacement for D900A or D90E

- The Dispenser pack D900A3 includes a plug-in Power supply.

- Plug in the existing ‘Cable set D90E/D900A-C900’ to the RJ12 jack on the back of the D900A3 dispenser.

- NOTE: When replacing an existing D90E dispenser, consider the dispenser weight difference with the D900A3 weighing an additional 2.2 Kg (4.9 lb) more than the D90E.  For example, the D900A3 cannot be installed on the Counter Stand.

## Signal and Info 900  – replacement Indicator

- Indicator V2service pack includes plug-in V2 cable adapters for connecting existing V2 power supply and TOM-Net data cables to the V2service Indicator.

- For replacement of a V2 CD-Nr Indicator or single common display, set the V2service Indicator address = 20.

- For replacement of a V2 CD-SP Indicator, set the V2service Indicator address = 30.

- For replacement of V2 Service Point (SP) Indicators, set the V2service Indicator address as follows:

SP1 = 21	SP2 = 22	SP3 = 23	SP4 = 24	SP5 =25	SP6 = 26	SP7 = 27	SP8 = 28

SP9 = 29	 SP10 = 2A	SP11 = 2B	SP12 =2C	SP13 = 2D	SP14 = 2E	SP15 = 2F

NOTE: Duplicate addresses are not allowed.

- Connect existing power cable to the V2service Indicator with the ‘Connection adapter V2 cable - V3 DC plug’.

- Connect the existing data cable to the V2service Indicator with the ‘Connection adapter V2 cable - V3 RJ10 plug’.   Connect the WHITE lead to Pin2-Signal A, brown lead to Pin3-Signal B and the cable shield to Pin1-GND.

## Signal and Info 900  – K900 replacement for C900

- NOTE: The C900S or C900S-PC MASTER cannot be replaced with a K900 unit.

- Connect existing power cable to the K900 with the ‘Connection adapter V2 cable - V3 DC plug’.

- Set the K900 address.  During K900 start-up, hold down the L key to open the address setting routing.  Then, press the R key first to display the address selection starting with 41.   Select the applicable Service Point address as follows:

SP1 = 41	SP2 = 42	SP3 = 43	SP4 = 44	SP5 =45	SP6 = 46	SP7 = 47	SP8 = 48

SP9 = 49	 SP10 = 4A	SP11 = 4B	SP12 =4C	SP13 = 4D	SP14 = 4E	SP15 = 4F

NOTE: Duplicate addresses are not allowed.

Hold down the L key to save the new address setting, which takes effect on next power ON.

- Connect the existing data cable to the K900 with the ‘Connection adapter V2 cable - V3 RJ10 plug’.   Connect the WHITE lead to Pin2-Signal A, brown lead to Pin3-Signal B and the cable shield to Pin1-GND.

- NOTE: Service Point direction lamps cannot be used with K900 units in V2 systems.

## Signal and Info 900 Parallel  – expansion SP Indicator and K900

- Indicator PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- For expansion of Service Point Indicators, set PLUS pack Indicator address as follows:

SP1 = 21	SP2 = 22	SP3 = 23	SP4 = 24	SP5 =25	SP6 = 26	SP7 = 27	SP8 = 28

SP9 = 29	 SP10 = 2A	SP11 = 2B	SP12 =2C	SP13 = 2D	SP14 = 2E	SP15 = 2F

NOTE: Duplicate addresses are not allowed.

- For expansion of Service Point keypads, set PLUS pack K900 address as follows:

SP1 = 41	SP2 = 42	SP3 = 43	SP4 = 44	SP5 =45	SP6 = 46	SP7 = 47	SP8 = 48

SP9 = 49	 SP10 = 4A	SP11 = 4B	SP12 =4C	SP13 = 4D	SP14 = 4E	SP15 = 4F

NOTE: Duplicate addresses are not allowed.

- To connect the PLUS pack TOM-Net data cable to the V2 Indicator, cut off the RJ10 plug on the V2 Indicator end of the cable.  Then, connect the data cable leads to the COMMS connector on the V2 Indicator as follows; WHITE lead to A, BROWN lead to B and the cable shield to the shield ground (upside down T).

- NOTE: Service Point direction lamps cannot be used with K900 units in V2 systems.

## Signal and Info 900  – expansion with K900

- K900 PLUS packs include plug-in Power supply and plug-in TOM-Net data cable.

- For expansion of Service Point keypads, set PLUS pack K900 address as follows:

SP1 = 41	SP2 = 42	SP3 = 43	SP4 = 44	SP5 =45	SP6 = 46	SP7 = 47	SP8 = 48

SP9 = 49	 SP10 = 4A	SP11 = 4B	SP12 =4C	SP13 = 4D	SP14 = 4E	SP15 = 4F

NOTE: Duplicate addresses are not allowed.

- To connect the PLUS pack TOM-Net data cable to the end C900, cut off the RJ10 plug on the C900 end of the cable.  Then, connect the data cable leads to the COMMS connector on the C900 as follows; WHITE lead to A, BROWN lead to B and the cable shield to the shield ground (upside down T).

- NOTE: Service Point direction lamps cannot be used with K900 units in V2 systems.

## Connection adapter V2 cable - V3 RJ10 plug, pin out

# Text boxes

Max = 220

Indicators + SL900 / system

Max = 30

K900 / system

PLUS pack K900

SP30 max

TOM-Net data cable

SLAVE

Maximum number of network units per system = 256 for V3 (32 for V2).

SP15 Max

TOM-Net total length can be 610 m (2000 ft).

TOM-Net

data cable

MASTER

NOTE:  Plug-in data cables are not designed to be field-fabricated.  Original Turn-O-Matic plug-in mating cables must be used to ensure proper connections and system operation.

CAUTION: There is no standard for DC jack & plug tolerances and not all DC plugs will fit correctly into the DC jacks on TOM units.  DO NOT USE A DC PLUG THAT MATES TOO TIGHTLY AND MUST BE FORCED INTO THE PLUG AS THIS WILL DAMAGE THE TOM UNIT AND VOID THE WARRANTY.

Connection for data: All units

Connection for Push Buttons in S3 system

Connection for Indicator cascade

The MASTER sends queries and commands to SLAVE units and input SLAVE units respond to queries with digital data on the 2-wire TOM-Net by changing the relative voltage between lines A and B.  When VA < VB, the data is a binary 1 and when VA > VB, the data is a binary 0.

The V3 TOM-Net data transmission rate is 19200 bps (bits per second) and the V2 data rate is 4800 bps.

START packs with 3-digit Indicator INR903 optional.

Indicator power supply not shown.

SLAVE

Only one MASTER per system, can be in any position on the chain.

Plug-in terminators

on end units to prevent data echoes.

SLAVE

START pack M32 CS

Dispenser D900

Counter Stand

(CS) optional

SLAVE

Dispenser D900

Counter Stand

(CS) optional

Max = 220

Indicators + SL900 / system

SP2

PLUS pack K900

SP1

PLUS pack K900

Dispenser D900

Counter Stand

(CS) optional

PLUS pack CDR22

PLUS pack D900A3

System Controller SC900

Keypad

K900

PLUS pack with 3-digit Indicator INR903 optional.

SC900, D900A3, Indicator and K900 power supply not shown.

TOM-Net

data cable

START pack L3

Dispenser D900A3

MASTER

Set TOM-Net addresses before installation for PLUS pack units:

Service ‘A’	Service ‘B’	Service ‘C’	Service ‘D’	Service ‘E’

D900A3 = A     	D900A3 = B     	D900A3 = C	D900A3 = D	D900A3 = E

Service Indicator = C1	Service Indicator = C2	Service Indicator = C3	Service Indicator = C4	Service Indicator = C5

Recall Indicator = CA	Recall Indicator = CB	Recall Indicator = CC	Recall Indicator = CD	Recall Indicator = CE

HCW Alert Signal = B1	HCW Alert Signal = B2	HCW Alert Signal = B3	HCW Alert Signal = B4	HCW Alert Signal = B5

Connection for power:

## All units, 12VAC or 15VDC

Mating connector: RJ10 plug

Mating connector: DC plug 2.5 mm

RJ10 jack

(4P4C) mm

DC jack

2.5 mm

START pack L3

Keypad

K900

Indicator INR902

PLUS pack with 3-digit Indicator INR903 optional.

SC900, D900A3, Indicator and K900 power supply not shown.

PLUS pack K900

SP2

START pack S32 RF CS

Keypad

K900

Dispenser D900

Counter Stand

(CS) optional

Push Button PB900 (-)

TOM-Net

data cable

Indicator INR902 RF

Push Button PB900 (-)

Wireless Push Button RFv2

Keypad

K900

PLUS packs with 3-digit Indicator INR903 optional.

Indicator and K900 power supply not shown.

Max = 15

K900 / system

Max = 241

Indicators / system

MASTER

SP2

SP1

CDR22

(Customer

Direction display)

Keypad

K900

START pack with 3-digit Indicator INR903 optional.

Indicator and K900 power supply not shown.

TOM-Net

data cable

START pack M32 Par CS

Keypad

K900

SP1

PLUS pack CDR22

Dispenser D900

Counter Stand

(CS) optional

TOM-Net

data cable

PLUS pack INR902

TOM-Net

data cable

SP2

SP1

Keypad

K900

Dispenser D900

Counter Stand

(CS) optional

PLUS pack INR902

Max = 15

K900 / system

MASTER

MASTER

START pack M32 Par CS

PLUS packs with 3-digit Indicator INR903 optional.

Indicator and K900 power supply not shown.

START pack M32 Par CS

Dispenser D900

Counter Stand

(CS) optional

MASTER

Dispenser D900A3

SYSTEM

MASTER

SP 2

SP 1

SP2

SP1

TOM-Net

data cable

MASTER

PLUS pack K900

PLUS pack INR902

Max = 241

Indicators / system

PLUS packs with 3-digit Indicator INR903 optional.

Indicator and K900 power supply not shown.

Service ‘B’

SP1

START pack with 3-digit Indicator INR903 optional.

Indicator and K900 power supply not shown.

Service ‘A’

Service ‘B’

Service ‘A’

HCW Alert Signal

START pack M32 Par CS

TOM-Net

data cable

Expansion

SL900, SP marking lamps

(max 15 total)

Max = 220

Indicators + SL900 / system

Indicator, K900 and SL900 power supply not shown.

PLUS packs with 3-digit Indicator INR903 optional.

Indicator power supply not shown.

Max = 15 PB / system

Max = 256

Indicators / system

PLUS pack K900

TOM-Net

data cable

Keypad

K900

PLUS pack SL900x2

TOM-Net

data cable

TOM-Net

data cable

MASTER

PLUS packs with 3-digit Indicator INR903 optional.  SC900, D900A3, Indicator, SL900 and K900 power supply not shown.

START pack L3

Keypad

K900

MASTER

PLUS pack INR902

System Controller SC900

TOM-Net

data cable

Keypad

K900

SP2

PLUS pack INR902

PLUS pack INR902

Wireless Push Button

SP1

MASTER

Max = 220

Indicators + SL900 / system

PLUS pack K900

SP1

PLUS pack D900A3

PLUS pack K900

PLUS pack SL900x2

PLUS pack INR902

Max = no limit

SLAVE

Wireless Push Button

Max = 256

Indicators / system

Wireless Push Button RFv2

PLUS packs with 3-digit Indicator INR903 optional.

Indicator power supply not shown.

PLUS pack INR902

PLUS pack D900A3

Expansion

Keypad K900

(max 30 total)

Max = 5

D900A3 / system

SLAVE

Dispenser D900

Counter Stand

(CS) optional

TOM-Net

data cable

Keypad

K900

PLUS pack SL900x2

PLUS pack K900

SP30 max

Max = 30

K900 / system

Max = 220

Indicators + SL900 / system

PLUS pack D900A3

SP30 max

START pack M32 CS

Service ‘B’

Wireless Push Button

Service ‘A’

Max = 30

K900 / system

PLUS pack K900

PLUS pack D900A3

Dispenser D900

Counter Stand

(CS) optional

SP30 max

PLUS pack K900

START pack S32 RF CS

SP1

PLUS pack K900

System Controller SC900

SP1

PLUS pack CDR22

PLUS pack D900A3

System Controller SC900

Keypad

K900

PLUS pack with 3-digit Indicator INR903 optional.

SC900, D900A3, Indicator, SL900 and K900 power supply not shown.

PLUS pack K900

SP3

MASTER

PLUS pack INR902

TOM-Net

data cable

START pack L3

Dispenser D900A3

START pack S32 PB CS

Hard-wired Push Button

SP2

MASTER

PB900 (+) plug-in set

PB900 (+) plug-in set

PLUS pack INR902

SLAVE

TOM-Net

data cable

Dispenser D900

Counter Stand

(CS) optional

START pack S32 PB CS

START packs with 3-digit Indicator INR903 optional.

Indicator power supply not shown.

SLAVE

PLUS pack INR902

Push Button PB900 (-)

Push Button PB900 (-)

Max = 220

Indicators + SL900 / system

PLUS pack with 3-digit Indicator INR903 optional.

SC900, D900A3, Indicator and K900 power supply not shown.

Max = 30

K900 / system

TOM-Net

data cable

START pack L3

PLUS pack

K900

Dispenser D900A3

PLUS pack D900A3

System Controller SC900

MASTER

PLUS pack K900

SP30 max

PLUS pack CDR22

Max = 30

K900 / system

PLUS pack K900

SP1

SP2

Max = 30

K900 / system

PLUS pack

K900

SP1

PLUS pack INR902

PLUS pack SL900x2

PLUS pack INR902

Recall Service Indicator

PLUS pack K900

PLUS pack INR902

PLUS pack D900A3

System Controller SC900

Keypad

K900

PLUS pack with 3-digit Indicator INR903 optional.  SC900, D900A3, Indicator, SL900 and K900 power supply not shown.

TOM-Net

data cable

START pack L3

MASTER

HCW Alert Signal

Service Indicator Extension

Service ‘B’

Service ‘A’

Service ‘A’

Service ‘B’

Service ‘B’

Max = 5

D900A3 / system

PLUS pack K900

Max = 30

K900 / system

PLUS pack

K900

Service ‘A’

PLUS pack SL900x2

PLUS pack INR902

PLUS pack D900A3

PLUS pack K900

PLUS pack INR902

PLUS pack D900A3

HCW Alert Signal

PLUS pack INR902

PLUS pack with 3-digit Indicator INR903 optional.

SC900, D900A3, Indicator and K900 power supply not shown.

PLUS pack INR902

Max = 220

Indicators + SL900 / system

Service Indicator Extension

HCW Alert Signal

Recall Service Indicator

Max = 220

Indicators + SL900 / system

SP30 max

Max = 220

Indicators + SL900 / system

Max = 30

K900 / system

PLUS pack CDR22

SP30 max

MASTER

PLUS pack K900

SP1

PLUS pack K900

PLUS pack CDR22

PLUS pack D900A3

System Controller SC900

Keypad

K900

PLUS pack with 3-digit Indicator INR903 optional.

SC900, D900A3, Indicator and K900 power supply not shown.

TOM-Net

data cable

START pack L3

Dispenser D900A3

MASTER

System Controller SC900

HSP

Indicator

TOM-Net

data cable

START pack L3

Dispenser D900A3

MASTER

PLUS pack INR902

Dispenser D900

Counter Stand

(CS) optional

START pack S32 PB CS

Wireless Push Button

Wireless Push Button RFv2

Push Button PB900 (-)

SLAVE

Indicator INR902 V2service

START pack S32 RF CS

Hard-wired Push Button

TOM-Net

data cable

Indicator INR902 RF

Push Button PB900 (-)

Indicator INR902

Dispenser D900

Counter Stand

(CS) optional

MASTER

TOM-Net addresses are pre-set for START pack units:

Indicator = 51

PLUS packs with 3-digit Indicator INR903 optional.

Indicator power supply not shown.

Max = no limit

Max = 256

Indicators / system

PB900 (+) plug-in set

PB900 (+) plug-in set

SLAVE

PLUS pack INR902

SLAVE

PLUS pack INR902

TOM-Net

data cable

Push Button PB900 (-)

Push Button PB900 (-)

START pack S32 PB CS

Dispenser D900

Counter Stand

(CS) optional

MASTER

TOM-Net addresses are pre-set for START pack units:

Indicator = 51 (MASTER)

Set TOM-Net addresses for PLUS pack units:

Indicator = 50 (SLAVE)

12VAC/15VDC

DC plug 2.5 mm

(use only TOM power supplies)

Indicator IN902 / 903

Keypad

K900

Dispenser

D900A3

System Controller

SC900

Signal Lamp

SL900

Use power extension with angled plug included with dispenser.

On back of Indicator, at the top

On bottom of K900

On top

of SL900

On LED indicator end of SC900

RJ10 modular plug

(use only TOM data cables)

Indicator IN902 / 903

TOM-Net

data I/O

Push Button (- / +)

Cascade In

Cascade Out

Keypad

K900

TOM-Net

data I/O

Indicator IN902 / 903

TOM-Net

data I/O

Signal Lamp

SL900

TOM-Net

data I/O

TOM-Net

data I/O

System Controller

SC900

Dispenser

D900A3

Keypad

K900

Rotate address switches with a small screwdriver.

Connect power.  Hold down L key during startup sequence.

Rotate address switch with a small screwdriver.

Change address

+ with ENTER key

or – with R key.

Hold down L key for 3+ seconds to save new address setting (takes affect on new power ON).

Rotate address switch with a small screwdriver.

Dispenser

D900A3

Signal Lamp

SL900

Wireless Push Button

PLUS packs with 3-digit Indicator INR903 optional.

Indicator power supply not shown.

Max = 15 PB / system

Max = 256

Indicators / system

Wireless Push Button RFv2

Wireless Push Button

SLAVE

PLUS pack INR902

SLAVE

PLUS pack INR902

TOM-Net

data cable

START pack S32 RF CS

Dispenser D900

Counter Stand

(CS) optional

MASTER

Set TOM-Net addresses for PLUS pack units:

Indicator = 50 (SLAVE)

TOM-Net addresses are pre-set for START pack units:

Indicator = 51 (MASTER)

Keypad

K900

START pack with 3-digit Indicator INR903 optional.

Indicator and K900 power supply not shown.

TOM-Net

data cable

START pack M32 CS

Dispenser D900

Counter Stand

(CS) optional

MASTER

TOM-Net addresses are pre-set for START pack units:

Indicator = 50

K900 = 71

SP2

SP1

Set TOM-Net addresses before installation for PLUS pack units:

Indicator = 50		K900 (Nr.6) = 76	K900 (Nr.11) = 7B

K900 (Nr.2) = 72	K900 (Nr.7) = 77	K900 (Nr.12) = 7C

K900 (Nr.3) = 73	K900 (Nr.8) = 78	K900 (Nr.13) = 7D

K900 (Nr.4) = 74	K900 (Nr.9) = 79	K900 (Nr.14) = 7E

K900 (Nr.5) = 75	K900 (Nr.10) = 7A	K900 (Nr.15) = 7F

NOTE: NO DUPLICATE K900 ADDRESSES ALLOWED!

PLUS pack K900

PLUS packs with 3-digit Indicator INR903 optional.

Indicator and K900 power supply not shown.

Max = 15

K900 / system

Max = 241

Indicators / system

PLUS pack K900

PLUS pack INR902

PLUS pack INR902

TOM-Net

data cable

MASTER

Keypad

K900

TOM-Net

data cable

START pack M32 CS

Dispenser D900

Counter Stand

(CS) optional

TOM-Net addresses are pre-set for START pack units:

Indicator = 50

K900 = 71

CDR22

(Customer

Direction display)

Keypad

K900

START pack with 3-digit Indicator INR903 optional.

Indicator and K900 power supply not shown.

TOM-Net

data cable

START pack M32 Par CS

Dispenser D900

Counter Stand

(CS) optional

MASTER

TOM-Net addresses are pre-set for START pack units:

Indicator CD-Nr = 50

Indicator CD-SP = 60

K900 SP1 = 71

K900 SP2 = 72

SP15 Max

SP3

PLUS pack K900

PLUS packs with 3-digit Indicator INR903 optional.

Indicator and K900 power supply not shown.

Max = 15

K900 / system

Max = 241

Indicators / system

PLUS pack K900

PLUS pack CDR22

TOM-Net

data cable

SP2

SP1

Keypad

K900

TOM-Net

data cable

START pack M32 Par CS

Dispenser D900

Counter Stand

(CS) optional

MASTER

Set TOM-Net addresses before installation for PLUS pack units:

Indicator CD-Nr = 50		K900 SP6 = 76	K900 SP11 = 7B

Indicator CD-SP = 60		K900 SP7 = 77	K900 SP12 = 7C

K900 SP3 = 73		K900 SP8 = 78	K900 SP13 = 7D

K900 SP4 = 74		K900 SP9 = 79	K900 SP14 = 7E

K900 SP5 = 75		K900 SP10 = 7A	K900 SP15 = 7F

NOTE: NO DUPLICATE K900 ADDRESSES ALLOWED!

TOM-Net addresses are pre-set for START pack units:

Indicator CD-Nr = 50

Indicator CD-SP = 60

K900 SP1 = 71

K900 SP2 = 72

SP2

SP1

PLUS pack INR902

PLUS packs with 3-digit Indicator INR903 optional.

Indicator and K900 power supply not shown.

PLUS pack INR902

TOM-Net

data cable

SP2

SP1

Keypad

K900

START pack M32 Par CS

Dispenser D900

Counter Stand

(CS) optional

MASTER

Set TOM-Net addresses before installation for PLUS pack units:

Indicator SP1 = 51	Indicator SP4 = 54	Indicator SP7 = 57	Indicator SP10 = 5A	Indicator SP13 = 5D

Indicator SP2 = 52	Indicator SP5 = 55	Indicator SP8 = 58	Indicator SP11 = 5B	Indicator SP14 = 5E

Indicator SP3 = 53	Indicator SP6 = 56	Indicator SP9 = 59	Indicator SP12 = 5C	Indicator SP15 = 5F

SP2

SP1

Indicator, K900 and SL900 power supply not shown.

PLUS pack SL900x2

TOM-Net

data cable

SP2

SP1

Keypad

K900

START pack M32 Par CS

Dispenser D900

Counter Stand

(CS) optional

MASTER

Set TOM-Net addresses before installation for PLUS pack units:

SL900 SP1 = 91	SL900 SP4 = 94	SL900 SP7 = 97	SL900 SP10 = 9A	SL900 SP13 = 9D

SL900 SP2 = 92	SL900 SP5 = 95	SL900 SP8 = 98	SL900 SP11 = 9B	SL900 SP14 = 9E

SL900 SP3 = 93	SL900 SP6 = 96	SL900 SP9 = 99	SL900 SP12 = 9C	SL900 SP15 = 9F

PLUS pack K900

PLUS pack INR902

PLUS pack D900A3

System Controller SC900

Keypad

K900

PLUS pack with 3-digit Indicator INR903 optional.

SC900, D900A3, Indicator and K900 power supply not shown.

TOM-Net

data cable

START pack L3

Dispenser D900A3

MASTER

Set TOM-Net addresses before installation for PLUS pack units:

Indicator = C1

K900 = 71

D900A3 = A

PLUS pack INR902

PLUS pack INR902

Max = 30

K900 / system

PLUS pack

K900

PLUS pack SL900x2

PLUS pack K900

PLUS pack INR902

PLUS pack D900A3

System Controller SC900

Keypad

K900

TOM-Net

data cable

START pack L3

MASTER

Max = 220

Indicators + SL900 / system

PLUS pack with 3-digit Indicator INR903 optional.  SC900, D900A3, Indicator, SL900 and K900 power supply not shown.

Set TOM-Net addresses before installation for PLUS pack units:

Service Indicator = C1	Recall Service Indicator = CA	HCW Alert Signal = B1

K900 (Nr.2) = 72	K900 (Nr.8) = 78	K900 (Nr.14) = 7E	K900 (Nr.20) = 85 	K900 (Nr.26) = 8B

K900 (Nr.3) = 73	K900 (Nr.9) = 79	K900 (Nr.15) = 7F	K900 (Nr.21) = 86	K900 (Nr.27) = 8C

K900 (Nr.4) = 74	K900 (Nr.10) = 7A	K900 (Nr.16) = 81	K900 (Nr.22) = 87	K900 (Nr.28) = 8D

K900 (Nr.5) = 75	K900 (Nr.11) = 7B	K900 (Nr.17) = 82	K900 (Nr.23) = 88	K900 (Nr.29) = 8E

K900 (Nr.6) = 76	K900 (Nr.12) = 7C	K900 (Nr.18) = 83	K900 (Nr.24) = 89	K900 (Nr.30) = 8F

K900 (Nr.7) = 77	K900 (Nr.13) = 7D	K900 (Nr.19) = 84	K900 (Nr.25) = 8A

NOTE: NO DUPLICATE K900 ADDRESSES ALLOWED!

System Controller SC900

Keypad

K900

PLUS packs with 3-digit Indicator INR903 optional.  SC900, D900A3, Indicator, SL900 and K900 power supply not shown.

TOM-Net

data cable

START pack L3

MASTER

MASTER

START pack L3

TOM-Net

data cable

PLUS pack with 3-digit Indicator INR903 optional.  SC900, D900A3, Indicator and K900 power supply not shown.

Keypad

K900

System Controller SC900

PLUS pack D900A3

PLUS pack INR902

PLUS pack K900

PLUS pack

K900

Max = 30

K900 / system

PLUS pack INR902

PLUS pack INR902

PLUS pack INR902

DSN Indicator

HCW Indicator

AWT Indicator

Set TOM-Net addresses before installation for PLUS pack units:

Indicator CD-Nr = C1	Indicator CD-SP = D1

K900 SP1 = 71	K900 SP7 = 77	K900 SP13 = 7D	K900 SP19 = 84	K900 SP25 = 8A

K900 SP2 = 72	K900 SP8 = 78	K900 SP14 = 7E	K900 SP20 = 85	K900 SP26 = 8B

K900 SP3 = 73	K900 SP9 = 79	K900 SP15 = 7F	K900 SP21 = 86	K900 SP27 = 8C

K900 SP4 = 74	K900 SP10 = 7A	K900 SP16 = 81	K900 SP22 = 87	K900 SP28 = 8D

K900 SP5 = 75	K900 SP11 = 7B	K900 SP17 = 82	K900 SP23 = 88	K900 SP29 = 8E

K900 SP6 = 76	K900 SP12 = 7C	K900 SP18 = 83	K900 SP24 = 89	K900 SP30 = 8F

NOTE: NO DUPLICATE K900 ADDRESSES ALLOWED!

SP30 max

Max = 220

Indicators + SL900 / system

Max = 30

K900 / system

SP30 max

PLUS pack K900

SP1

PLUS pack K900

PLUS pack CDR22

PLUS pack D900A3

System Controller SC900

Keypad

K900

PLUS pack with 3-digit Indicator INR903 optional.

SC900, D900A3, Indicator and K900 power supply not shown.

TOM-Net

data cable

START pack L3

Dispenser D900A3

MASTER

SP1

PLUS pack INR902

PLUS pack INR902

Set TOM-Net addresses before installation for PLUS pack units:

Indicator SP1 = 51	Indicator SP7 = 57	Indicator SP13 = 5D	Indicator SP19 = 64	Indicator SP25 = 6A

Indicator SP2 = 52	Indicator SP8 = 58	Indicator SP14 = 5E	Indicator SP20 = 65	Indicator SP26 = 6B

Indicator SP3 = 53	Indicator SP9 = 59	Indicator SP15 = 5F	Indicator SP21 = 66	Indicator SP27 = 6C

Indicator SP4 = 54	Indicator SP10 = 5A	Indicator SP16 = 61	Indicator SP22 = 67	Indicator SP28 = 6D

Indicator SP5 = 55	Indicator SP11 = 5B	Indicator SP17 = 62	Indicator SP23 = 68	Indicator SP29 = 6E

Indicator SP6 = 56	Indicator SP12 = 5C	Indicator SP18 = 63	Indicator SP24 = 69	Indicator SP30 = 6F

PLUS pack SL900x2

SP30 max

Max = 220

Indicators + SL900 / system

Max = 30

K900 / system

SP30 max

PLUS pack K900

SP1

PLUS pack K900

PLUS pack CDR22

PLUS pack D900A3

System Controller SC900

Keypad

K900

PLUS pack with 3-digit Indicator INR903 optional.

SC900, D900A3, Indicator, SL900 and K900 power supply not shown.

TOM-Net

data cable

START pack L3

Dispenser D900A3

MASTER

SP1

Set TOM-Net addresses before installation for PLUS pack units:

SL900 SP1 = 91	SL900 SP7 = 97	SL900 SP13 = 9D	SL900 SP19 = A4	SL900 SP25 = AA

SL900 SP2 = 92	SL900 SP8 = 98	SL900 SP14 = 9E	SL900 SP20 = A5	SL900 SP26 = AB

SL900 SP3 = 93	SL900 SP9 = 99	SL900 SP15 = 9F	SL900 SP21 = A6	SL900 SP27 = AC

SL900 SP4 = 94	SL900 SP10 = 9A	SL900 SP16 = A1	SL900 SP22 = A7	SL900 SP28 = AD

SL900 SP5 = 95	SL900 SP11 = 9B	SL900 SP17 = A2	SL900 SP23 = A8	SL900 SP29 = AE

SL900 SP6 = 96	SL900 SP12 = 9C	SL900 SP18 = A3	SL900 SP24 = A9	SL900 SP30 = AF

AWT Indicator

HCW Indicator

DSN Indicator

PLUS pack INR902

PLUS pack INR902

PLUS pack INR902

Max = 30

K900 / system

PLUS pack

K900

PLUS pack K900

PLUS pack INR902

PLUS pack D900A3

System Controller SC900

Keypad

K900

PLUS pack with 3-digit Indicator INR903 optional.  SC900, D900A3, Indicator and K900 power supply not shown.

TOM-Net

data cable

START pack L3

MASTER

Max = 220

Indicators + SL900 / system

Set TOM-Net addresses before installation for PLUS pack units:

Service ‘A’	Service ‘B’	Service ‘C’	Service ‘D’	Service ‘E’

AWT Indicator = 3A     	AWT Indicator = 3B     	AWT Indicator = 3C     	AWT Indicator = 3D     	AWT Indicator = 3E

DSN Indicator = 31	DSN Indicator = 32	DSN Indicator = 33	DSN Indicator = 34	DSN Indicator = 35

HCW Indicator = BA	HCW Indicator = BB	HCW Indicator = BC	HCW Indicator = BD	HCW Indicator = BE

HSP

Indicator

Max = 220

Indicators + SL900 / system

Max = 30

K900 / system

SP30 max

PLUS pack K900

SP1

PLUS pack K900

PLUS pack CDR22

PLUS pack D900A3

System Controller SC900

Keypad

K900

PLUS pack with 3-digit Indicator INR903 optional.

SC900, D900A3, Indicator and K900 power supply not shown.

TOM-Net

data cable

START pack L3

Dispenser D900A3

MASTER

PLUS pack INR902

Set TOM-Net addresses for PLUS pack units:

HSP Indicator = B9

EA (Error Address)

Indicator has been set to an invalid TOM-Net address.  This message applies to all systems and is displayed on Indicator startup.

After briefly displaying the ‘EA’ message, the Indicator then briefly displays the invalid address setting (example = 81).  This display sequence then cycles continuously.

Corrective actions:

- Change the Indicator address to a valid TOM-Net Indicator address.

- If the Indicator is set to a valid TOM-Net address, the rotary address switches or internal connections are faulty.  Replace the Indicator.

Ed (Error Duplicate)

There are duplicate MASTER Indicators on the system, i.e. more than one Indicator set to Address 51.

This message only applies to the system S3 and is displayed on Indicator startup.

Corrective actions:

- Change any duplicate MASTER Indicator addresses to Address 50.

oFF (K900 logged OFF)

The K900 is not logged ON to a Service.

Hold down the L key 3+ seconds to open the logon process.  Press the ENTER key to step through the selections ‘Aon’, ‘bon’, ‘Con’, ‘don’ and ‘Eon’ Service Types or ‘LoFF’ to log the K900 OFF the system.

Hold down the L key 3+ seconds to activate the selection.

EC (Error Communication)

The ‘EC’ message applies to both systems M3 and L3.

If ‘EC’ is displayed on system startup, more than one K900 has been set to the same address.

Corrective action:

- Check for duplicate K900 address settings and change to a non-duplicate address.

If ‘EC’ is displayed during system operation, the message can be removed on the K900 displaying the message by holding down the F key 3+ seconds to display ‘F-00’ and pressing the ENTER key.

If the ‘EC’ message reappears:

- Check for faulty TOM-Net data cable connections and replace any suspect data cables.

If the ‘EC’ message does not reappear:

- A unit on the system has been powered OFF, most notably a dispenser D900A3.  When the D900A3 is powered ON again, the dispenser will be Off-line and the message ‘$.doL’  ($ = service ‘A, b, C, d or E’) will be displayed.

- A unit has been disconnected and reconnected to the system (hot swapped).

- There are duplicate Indicator addresses on an L3 system, which is allowed.  In scanning for active devices, it can happen that the SC900 receives answers from both Indicators at almost the same time and the misread data is seen as an ‘EC’ error.

$.doL (Dispenser OFF line)

The dispenser for the $=Service Type (example ‘A’) is not ON line.

Press the D key.  K900 displays A_ _ _  (example) for input of start ticket number.   Key in the start ticket number (all 3 digits) and press the D key again.  K900 displays A.- - -  showing that it is ready for normal operation.

Note: Pressing the D key without input of a ticket number will assume the last dispensed number as the start number.

$.SoL (Service OFF line)

There are customers waiting for first service call in $=Service Type (example ‘B’) and no K900 is logged ON to that Service.

Hold down the L key 3+ seconds to open the logon process.  Press the ENTER key to step through the selections ‘Aon’, ‘bon’, ‘Con’, ‘don’ and ‘Eon’ Service Types.   Select the OFF line Service Type and hold down the L key 3+ seconds to log ON.

$.dbF (Data buffer full)

The active service buffer for the $=Service Type (example ‘A’) is nearly full, nearing the maximum of 250 customers waiting for first call or recall service.

When the data buffer is full, new customer numbers will overwrite the oldest numbers in the buffer.

Notes: If there are many unwanted recall numbers, set F24 SAVE type to Manual Save (default) instead of Auto Save.

Recall numbers can be scrolled and optionally removed when they are displayed on the K900 by pressing the E key to END service.

$.dLt (Dispenser low ticket level)

The dispenser for the $=Service Type (example ‘A’) has reached the tickets remaining alert level (set with F43, pre-set default = 100 tickets remaining).

To change ticket roll, hold down the D key 3+ seconds to put the dispenser OFF line.

Set in the new ticket roll and take a ticket before closing the dispenser cover.  Press the D key and input this ticket number for the start ticket number.  Press the D key to put the dispenser ON line.

Note:

These warning messages can be removed from the K900 display.

Hold down the F key 3+ seconds until the K900 displays F-00.  Press the ENTER key to remove the message display.

PLUS pack INR902

TOM-Net

data cable

PLUS packs with 3-digit Indicator INR903 optional.

Indicator power supply not shown.

Indicator INR902 V2service

PLUS packs with 3-digit Indicator INR903 optional.

Indicator power supply not shown.

PLUS pack INR902

TOM-Net

data cable

PB900 (+) plug-in set

Wireless Push Button set RFv2

Indicator INR902 V2service

PLUS packs with 3-digit Indicator INR903 optional.

Indicator power supply not shown.

PLUS pack INR902

TOM-Net

data cable

Keypad K900

Connection adapter V2 cable - V3 DC plug

Connection adapter V2 cable - V3 RJ10 plug

Indicator INR902 V2service

PLUS packs with 3-digit Indicator INR903 optional.

Indicator and K900 power supply not shown.

PLUS pack INR902

TOM-Net

data cable

PLUS pack K900

SP15 max

Connection adapter V2 cable - V3 RJ10 plug

Connection adapter V2 cable - V3 DC plug

Keypad K900

Dispenser pack D900A3

C900S or C900S-PC MASTER

C900S or C900S-PC MASTER

Indicator INR902 V2service

C900S or C900S-PC MASTER

PLUS pack K900

SP15 max

PLUS packs with 3-digit Indicator INR903 optional.

Indicator and K900 power supply not shown.

PLUS pack INR902

TOM-Net

data cable

C900S or C900S-PC MASTER

Connection adapter V2 cable - V3 RJ10 plug

Connection adapter V2 cable - V3 DC plug

Keypad K900

Max = 15

C900 + K900 / system

PLUS pack K900

PIN MARKING

The output terminal pin marking for the RJ adapter should be as shown.

It is possible that cable adapters are incorrectly marked with the pin-marking label attached upside down.

For TOM-Net data cable connections, check the pin-marking label to be sure that it agrees with correct pin marking shown.

TOM-Net connection

Push Button connection